The following specification text has been prepared to assist design professionals in the preparation of a specification section covering architectural glass including textured, etched, back-painted, light-diffusing, patterned, luminous, rice paper, dichroic, mouth-blown, and other decorative and specialty glasses.

Utilize these paragraphs to insert text into Specification Section 08 8000 - Glazing or similarly titled section governing this work.

For assistance on the use of the products in this section, contact  S.A. Bendheim, Ltd. by calling 800-606-7621, by email at sales@bendheim.com, or visit their website at www.bendheim.com.

PART 1 - GENERAL

SUBMITTALS

Include the following for submission of samples for verification of type, color, and pattern.

A.	Samples [10 x 12] [2-5/8 x 5] [__ x __] inch glass samples showing type, color, and pattern.

QUALITY ASSURANCE

Include the following for glass in locations subject to human impact.

A.	Regulatory Requirements:

1.	Provide safety glass for locations subject to human impact as required by [Building Code.] [____.]

2.	Safety glass: Tested and labeled to CPSC 16 CFR 1201. Safety film not acceptable as alternative to tempered or laminated glass.

PART 2 - PRODUCTS

MATERIALS - GENERAL

Include one or more of the following as applicable to glass types required for project.

A.	Annealed Glass: Comply with ASTM C1036.

B.	Tempered Glass:

1.	Comply with ASTM C1048, ANSI Z97.1, and CPSC 16 CFR 1201, Category II.

2.	Process in horizontal position so that inherent roller distortion will run parallel to building floor lines after installation.

C.	Laminated Glass:

1.	Comply with ASTM C1172, ANSI Z97.1, and CPSC 16 CFR 1201, Category II.

2.	Laminate glass by manufacturer's standard heat and pressure process.

D.	Glass Identification:

1.	Apply manufacturer's label indicating type and thickness to each light of glass. Show position of exterior face when installed, where applicable.

The following paragraph ensures compliance with Building Code requirements, but may be deleted if a letter certifying to tempering or laminating of glass is acceptable to the building owner and local code officials.

2.	Etch manufacturer's label on each light of tempered or laminated glass.

GLASS MATERIALS

Include one or more of the following depending on specific glass chosen for project. Refer to S.A. Bendheim, Ltd. technical information or contact S.A. Bendheim, Ltd. for assistance in selecting products and editing the following paragraphs to suit project requirements.

A.	Textured Glass:

1.	Product: [____] by S.A. Bendheim, Ltd., 800-606-7621, www.bendheim.com; [or approved substitute.] [substitutions not permitted.]

2.	Description: [To match Architect’s sample.] [Geometric.] [Organic.] [Linear.] [Annealed.]

3.	Type: [Tempered.] [Laminated.] [Tempered and laminated.] [Back painted.]

4.	Thickness: [__] inch.

5.	Edge treatment: [Flat polished.] [Cut and seamed.] [Ground.] [Mitered.] [____.]

B.	EcoGlass:

1.	Product: [____] by S.A. Bendheim, Ltd., 800-606-7621, www.bendheim.com; [or approved substitute.] [substitutions not permitted.]

2.	Description: [To match Architect’s sample.] [Textured clear [annealed] [tempered] [laminated] [back-painted] glass.]

3.	Recycled content: Minimum 25 percent.

4.	Thickness: [__] inch.

5.	Edge treatment: [Flat polished.] [Cut and seamed.] [Ground.] [Mitered.] [____.]

C.	Etched Glass:

1.	Product: [____] by S.A. Bendheim, Ltd., 800-606-7621, www.bendheim.com; [or approved substitute.] [substitutions not permitted.]

2.	Description: [To match Architect’s sample.] [Chemically etched on [one side] [two sides.]

3.	Color: [Standard clear.] [Ultra clear low iron.] [____.]

4.	Pattern: [One side.] [Two sides.] [Back painted.]

5.	Type: [Annealed.] [Tempered.] [Laminated.]

6.	Thickness: [__] inch.

7.	Edge treatment: [Flat polished.] [Cut and seamed.] [Ground.] [Mitered.] [____.]

D.	[Back-Painted] [Mirror-Backed] Glass:

1	Product: [____] by S.A. Bendheim, Ltd., 800-606-7621, www.bendheim.com; [or approved substitute.] [substitutions not permitted.]

2.	Description: [To match Architect’s sample.] [Ultra-clear low-iron float glass.] [Water-based back-painted coating free from isocyanates and volatile organic compounds.]

3.	Color: To match [Bendheim sample No. [____].] [Pantone Color No. [____].] [Paint manufacturer’s Color No. [____] by [____].]

4.	Thickness: [__] inch.

5.	Edge treatment: [Flat polished.] [Cut and seamed.] [Ground.] [Mitered.] [____.]

E.	Laminated Glass:

1.	Product: [____] by S.A. Bendheim, Ltd., 800-606-7621, www.bendheim.com; [or approved substitute.] [substitutions not permitted.]

2.	Description: [To match Architect’s sample.] [Annealed.] [Tempered.] [[____] pattern.]

3.	Interlayer: Bridgestone EVA, Uvekol, or PVB.

4.	Overall thickness: [__] inch.

5.	Edge treatment: [Flat polished.] [Cut and seamed.] [Ground.] [Mitered.] [____.]

F.	Art Glass:

1.	Product: [____] by S.A. Bendheim, Ltd., 800-606-7621, www.bendheim.com; [or approved substitute.] [substitutions not permitted.]

2.	Description: [To match Architect’s sample.] [Laminated.]

3.	Thickness: [__] inch.